## Slide 1: Feasibility Study of PET Dynamic Imaging of [18F]DHMT for Quantification of Reactive Oxygen Species in the Myocardium of Large Animals
Journal of Nuclear Cardiology | Official Journal of the American Society of Nuclear Cardiology
Jing Wu, PhD,a,* Nabil E. Boutagy, PhD,b,* Zhengxin Cai, PhD,a Shu-fei Lin, PhD,a Ming-Qiang Zheng, PhD,a Attila Feher MD, PhD,b John Stendahl, MD, PhD,b Michael Kapinos,a Jean-Dominique Gallezot, PhD,a Hui Liu, PhD,a Tim Mulnix, PhD,a Wenjie Zhang, MD, PhD,a Marcel Lindemann, PhD,a Jo-ku Teng,a Edward J. Miller, MD, PhD,b Yiyun Huang, PhD, a Richard E. Carson, PhD,a Albert J. Sinusas, MD,a,b Chi Liu, PhD,a
aDepartment of Radiology and Biomedical Imaging, Yale School of Medicine, New Haven, Connecticut
bSection of Cardiovascular Medicine, Department of Medicine, Yale Translational Research Imaging Center, Yale School of Medicine, New Haven, Connecticut
*Jing Wu and Nabil E. Boutagy contributed equally to this work.
Copyright American Society of Nuclear Cardiology
Jing Wu, PhD
Nabil E. Boutagy, PhD

## Slide 2: BACKGROUND
1- Excessive reactive oxygen species (ROS) production has been implicated in the development and progression of a variety of cardiovascular diseases (CVDs).
2- Currently, the noninvasive measurement of ROS is limited to circulating or urinary biomarkers that are not specific to the myocardium.
3- For specific measurement of myocardial ROS production, our group has recently demonstrated the ability of static PET imaging for a novel tracer, [18F]DHMT, to detect an elevation in myocardial superoxide production in a rodent model of progressive anthracycline-induced cardiotoxicity.
4- In this study, we aimed to develop a dynamic PET imaging technique for [18F]DHMT to allow for absolute quantification of myocardial ROS production in a large animal model.
Copyright American Society of Nuclear Cardiology
Journal of Nuclear Cardiology | Official Journal of the American Society of Nuclear Cardiology

## Slide 3: METHODS
Study type:(Select all that apply)
  Prospective/retrospective/randomized/double blind/placebo controlled/observational/case control/cohort/experimental
Study subjects: (one sentence summarizing included and/or excluded subjects):
  Seven retired female beagle breeders were included in this study. Of these, one animal also underwent a chronic-doxorubicin (DOX) dosing protocol to elicit progressive systolic dysfunction by receiving weekly doses of DOX HCl (1 mg/kg/week).
Study endpoints (chronic study):
  Primary end point(s): Cumulative DOX dose of 15 mg/kg was reached
  Secondary end point(s): A decline in LVEF below 50%.
Study variables
  Myocardial [18F]DHMT uptake (Ki, SUV, LV-to-blood pool SUV ratio)
  Plasma [18F]DHMT metabolite analysis
Copyright American Society of Nuclear Cardiology
Journal of Nuclear Cardiology | Official Journal of the American Society of Nuclear Cardiology

## Slide 4: RESULTS
Figure. Illustration of the kinetics of [18F]DHMT in the cardiomyocytes following the irreversible two-tissue (2Ti) compartment model. K1, k2 and k3 are the rate constants of [18F]DHMT movement between compartments, and Ki is the net influx rate of [18F]DHMT from the plasma into the irreversibly bound compartment.
Copyright American Society of Nuclear Cardiology
Journal of Nuclear Cardiology | Official Journal of the American Society of Nuclear Cardiology

## Slide 5: RESULTS
Table. LV SUV (60 - 90 min), LV-to-blood pool SUV ratio (60 - 90 min) and 2Ti derived Ki values for each study.
Copyright American Society of Nuclear Cardiology
Journal of Nuclear Cardiology | Official Journal of the American Society of Nuclear Cardiology
Study | Subject | DOX Dose (mg/kg) | SUV (g/mL) | SUV ratio | Ki (mL/min/cm3)
1 | Dog #1 | 0 | 1.91 | 2.56 | 0.0161
2 | Dog #2 | 0 | 1.61 | 2.08 | 0.0096
3 | Dog #3 | 0 | 2.15 | 1.90 | 0.0078
4 | Dog #4 | 0 | 1.13 | 2.01 | 0.0094
5 | Dog #5 | 0 | 1.51 | 1.99 | 0.0101
6 | Dog #6 | 0 | 2.22 | 3.17 | 0.0226
7 | Dog #7 | 3 | 1.09 | 2.00 | 0.0092
8 | Dog #7 | 7 | 1.21 | 1.88 | 0.0108
9 | Dog #7 | 12 | 1.30 | 2.07 | 0.0133
mean | Dogs #1-6 | 0 | 1.76 | 2.29 | 0.0126
SD | Dogs #1-6 | 0 | 0.42 | 0.49 | 0.0057

## Slide 6: CONCLUSIONS
1- We developed a dynamic PET imaging technique with full kinetic modeling and metabolite analysis for absolute quantification of the superoxide tracer, [18F]DHMT, in a large animal model.
2- We demonstrated that [18F]DHMT is an irreversible tracer and selected 2Ti as the optimal compartment model for kinetic modeling.
3- Patlak analysis was selected as the simplified graphical analysis method and was successfully used for generating high-quality parametric Ki images that had superior myocardium-to-blood contrast than static images.
4- The proposed technique for quantifying in vivo myocardial superoxide production from dynamic PET imaging of [18F]DHMT may provide prognostic information in CVD, such as heart failure, in which oxidative stress plays a key role in disease development and progression.
Copyright American Society of Nuclear Cardiology
Journal of Nuclear Cardiology | Official Journal of the American Society of Nuclear Cardiology